## Slide 1: Modeling the Operations of Electric Autonomous Taxis in New York City
Liang Hu and Jing Dong
Presented at 2017 INFORMS Annual Meeting, Houston, TX
October 23, 2017

## Slide 2: Why Electric Autonomous Taxis?
Introduction | Simulation | Optimization | Results | Summary
Conventional taxis
Ride
-
hailing
Electric
autonomous
vehicles (EAV)
Energy
source
•
gasoline
•
some electric
•
gasoline
•
some electric
•
electric
Search for
customers
•
cruising
•
by chance
•
cruising
+ waiting
•
drivers compete
•
relocating
+ waiting
•
collaborative
Customers’
delay
•
unknown to taxis
•
drivers do not care
•
optimal dispatch
•
reduce delay
Trip
distance
•
unknown to taxis
•
taxis w/o sufficient
range are not
assigned
•
unknown to taxis
Notes: delete unknown

## Slide 3: Model EAV Taxi Operations
t
t-1
t-2
Model operations based on status of both requests and taxis, over time, area by area
Requests
request time location wait time
EAV taxis
location SOC
Introduction | Simulation | Optimization | Results | Summary

## Slide 4: Taxi Trip Data in NYC
Introduction | Simulation | Optimization | Results | Summary
Data fields
  taxi ID
  pick-up GPS
  pick-up timestamp
  drop-off GPS
  drop-off timestamp
  occupied trip distance
trip dist. = 1.4413straight-line dist. + 0.1383 (unit: mi)
Estimate empty trip dist. by
Extract data of 500 taxis & the corresponding requests
Notes: delete unknown

## Slide 5: Assumptions for Simulation
Introduction | Simulation | Optimization | Results | Summary
Requests of customers
  location: pick-up GPS
  time: pick-up timestamp
  dist.: occupied trip dist.
EAV taxis
  location: drop-off GPS
  time: drop-off timestamp
  dist.: estimated trip dist.
Notes: Keep requests’ GPS unchanged. Consider pickup timestamp as the time of requesting taxis.

## Slide 6: Charging Stations in NYC
310 charging stations;
assume 50 kW fast chargers.
Source: US DOE
Introduction | Simulation | Optimization | Results | Summary

## Slide 7: Simulation Process
Introduction | Simulation | Optimization | Results | Summary
generate 500 EAV taxis
keep initial locations & timestamps
set random initial SOC [10%, 100%]
waiting
unserved requests & available taxis at
optimize dispatch
called
occupied
SOC≥10% at drop-off?
going to charging stations
charging to 100% SOC
not assigned
assigned
yes
no

## Slide 8: Decision Variables
available taxis and unserved requests at
Define binary decision variables
Introduction | Simulation | Optimization | Results | Summary
: index of an available taxi,
: index of an unserved request,
: taxi picks up request
: taxi does not pick up request

## Slide 9: Objective Function
: cost matrix (1) = time that has been delayed + time for pick-up
: cost matrix (2) = time that has been delayed + avg. wait time
minimize
total costs of the requests that can be served
total costs of the requests that cannot be served
Introduction | Simulation | Optimization | Results | Summary
differs by area

## Slide 10: Constraints (1): Sufficient EV Range
calculate the distance matrix
if > the taxi’s remaining range,
Introduction | Simulation | Optimization | Results | Summary
Notes: Check whether SOC is enough.

## Slide 11: Constraints (2)
Each taxi will server at most one customer
Each customer will be served by at most one taxi
Introduction | Simulation | Optimization | Results | Summary

## Slide 12: Solver
Gurobi 7.5.1
integer linear programming (ILP)
1440 time intervals
CPU Intel E5-1620 3.70GHz, RAM 16GB
~40 minutes
Introduction | Simulation | Optimization | Results | Summary

## Slide 13: Customer Wait Time Distribution
Introduction | Simulation | Optimization | Results | Summary
Only 0.5% of requests are not served
Average wait time is 4.7 minutes
95% of requests are served within 11 minutes

## Slide 14: Total Travel Distance of Taxis
Introduction | Simulation | Optimization | Results | Summary
Average travel distance reduces by 18%
126 mi
154 mi

## Slide 15: Ratio of Occupied/Total Travel Distance
Introduction | Simulation | Optimization | Results | Summary
EAV taxi system reduces empty trip distance from 49 mi to 23 mi
Average ratio of occupied distance increases from 69% to 82%
82%
69%

## Slide 16: Implications of Fleet Size
Chart: Fleet size reduces by
| 0 | 0.05 | 0.1 | 0.15 | 0.2
Unserved requests | 0.0045383 | 0.0049706 | 0.0052407 | 0.0059431 | 0.0062672
Unserved requests | 0.0045383 | 0.0049706 | 0.0052407 | 0.0059431 | 0.0062672
Chart: Fleet size reduces by
| 0 | 0.05 | 0.1 | 0.15 | 0.2
Unserved requests | 4.7077 | 5.6259 | 6.5756 | 8.9115 | 13.1358
Introduction | Simulation | Optimization | Results | Summary
Reduces fleet size by 5%~20%
Unserved requests remain at 0.5%~0.6%
Average delay is within 9 minutes when fleet size reduces by ≤15%
Average delay increases more significantly at 20% reduction

## Slide 17: Implications of Fleet Size
Chart: Fleet size reduces by
| 0 | 0.05 | 0.1 | 0.15 | 0.2
Unserved requests | 125.8808 | 132.8726 | 140.5245 | 148.4997 | 156.8032
Chart: Fleet size reduces by
| 0 | 0.05 | 0.1 | 0.15 | 0.2
Unserved requests | 0.81941 | 0.81493 | 0.80978 | 0.81147 | 0.81462
Chart: Fleet size reduces by
| 0 | 0.05 | 0.1 | 0.15 | 0.2
Unserved requests | 0.506 | 0.52652 | 0.53388 | 0.56435 | 0.58759
Introduction | Simulation | Optimization | Results | Summary
With smaller fleet size, EAV taxis become busier
  travel distance & ratio of occupied time increase almost linearly
Efficiency of current taxi system ≈ EAV taxis with 80% of fleet size
Ratio of occupied distance remains stable at 81%~82%
current taxis: 154

## Slide 18: Implications of Electric Range
Introduction | Simulation | Optimization | Results | Summary
Chart: Range (mi)
| 150 | 200 | 250 | 300
 | 0.0045924 | 0.0045383 | 0.0045383 | 0.0043762
 | 0.0045924 | 0.0045383 | 0.0045383 | 0.0043762
Chart: Range (mi)
| 150 | 200 | 250 | 300
 | 4.8373 | 4.7077 | 4.6052 | 4.7162
Chart: Range (mi)
| 150 | 200 | 250 | 300
Unserved requests | 125.8433 | 125.8808 | 125.8679 | 125.9489
Chart: Range (mi)
| 150 | 200 | 250 | 300
Unserved requests | 0.82038 | 0.81941 | 0.82034 | 0.8182
Chart: Range (mi)
| 150 | 200 | 250 | 300
Unserved requests | 0.51119 | 0.506 | 0.51546 | 0.50729
Range does not have considerable implications on request delays nor efficiency of EAV taxi systems
unserved requests: 0.5%
avg. delay: 4.6~4.8 min
avg. total travel dist.: 126 mi
avg. ratio of occupied dist.: 82%
avg. ratio of occupied time: 51%~52%
Notes: Probably due to 50 kW fast charging.

## Slide 19: Summary
EAV taxis improves efficiency of taxi systems
  less empty trips
  less energy consumption
EAV taxis has potential to reduce fleet size, while keep wait time at an acceptable level
  average delay is within 9 min when the fleet size is reduced by 15%
Introduction | Simulation | Optimization | Results | Summary

## Slide 20: Thank you
Corresponding author:
Dr. Jing Dong
jingdong@iastate.edu
Modeling the Operations of Electric Autonomous Taxis in New York City